## Slide 1: Satellite Hacks
At Layer 1

## Slide 2: The Plan
But Why?
What are satellites?
Basics
  Orbits
  Doppler Shift
Decoding NOAA WX Sats
Ham radio satellites
FOSS Ground Station Projects
Satellite SIGINT

## Slide 3
CTF in Space
Moonlighter Satellite
Notes: Yearly CTF to hack a satellite
Qualification in APRIL
Finals at Def Con
Our team placed 252 in qualification

## Slide 4
CTF in Space
Moonlighter Satellite
Qualification Rank
Notes: Our team placed 252 in qualification

## Slide 5: Satellites, how do they work?
Notes: Satellites usually mean artificial satellites
Common uses: Communication, imaging, earth observation, navigation, reconnaissance
Most sats have electrical component. Passive sat - big ball PAGEOS

## Slide 6: What can you do with Satellites?
Free Communications Relay
Listen to interesting signals
https://hamvillage.org/
Notes: Common element to most satellites are radio
Mission is radio based
Command and control
Free communications relay
Legal: Amateur Radio
  Free to use with a ham radio license
  LEO, MEO and GEO
Illegal: Pirate satellites
  Use transponders without permission
Listening:
Free TV
Satellite telemetry and mission status information
  SpaceX telem and video was unencrypted until March 2021 https://twitter.com/r2x0t/status/1375472068595187722
  Private moon landing

## Slide 7
Mark Mercer, CC BY-SA 3.0, via Wikimedia Commons
https://earthobservatory.nasa.gov/features/OrbitsCatalog
Notes: Three common orbits
LEO: Low earth orbit below 1,200 miles.
ISS is at 211 miles
MEO: Medium earth orbit
1,200 Miles to 22,000 miles
GPS satellites 12,500 miles
GEO: geosynchronouns and geostationary (GSO)
At 22,000 miles
HEO: High earth orbit
Above 22,000 miles
Molniya Orbit:
Russian for lightning
Coverage over polar region
3 satellites in a constellation for continuous coverage

## Slide 8: Doppler
Frequency of observed wave depends on the relative speed of the observer
Notes: Waves appear compressed, higher frequency as source approaches
Spread out, lower frequency, as it moves away

## Slide 9: Doppler
Notes: Satellites move fast enough to impact RF signals
As the satellite approaches the relative velocity is + at maximum speed when at AOS
When apogee, relative motion is 0 and no doppler shift
As moves away velocity - at maximum speed during LOS
Satellite communications need to correct for
uplink as seen by the satellite
Downlink as seen by the ground station

## Slide 10: printf(“Hello world.”)
WX Satellite Reception
Satellite | Frequency
NOAA-15 | 137.6200 MHz
NOAA-18 | 137.9125 MHz
NOAA-19 | 137.1000 MHz
Notes: Where to start?
WX Satellites are the hello world of satellite reception
Needed:
Receiver (traditional or SDR)
Antenna
Computer to decode

## Slide 11: printf(“Hello world.”)
Where are they?
TLE: Two Line elements
Notes: Software and websites available for satellite tracking
  Gpredict - Linux
  MacDoppler - Mac
  Orbitron - Window
  SatPC32 - Windows
  Iss Detector - Android

## Slide 12: printf(“Hello world.”)
WX Satellite Antenna
Notes: Doesn’t require expensive antennas
Needed:
Receiver (traditional or SDR)
Antenna
Computer to decode

## Slide 13: printf(“Hello world.”)
YouTube Tutorials
Instructables https://www.instructables.com/NOAA-Satellite-Signals-with-a-PVC-QFH-Antenna-and-/
Browser Based: https://apt.open-weather.community/
Notes: Many tutorials available for Win/Linux/Mac
Instructable showing how to construct antenna
Browser based solutions

## Slide 14: printf(“Hello world.”)
Image: https://www.instructables.com/NOAA-Satellite-Signals-with-a-PVC-QFH-Antenna-and-/

## Slide 15: Ham Radio Satellites
Telemetry Only
FM Repeater
Linear Transponder
Digital Repeater
AO-91
AO-7
Notes: Ham radio satellites are free and open to all licensed ham radio operators
Sizes range
  Cube Sat 10cm^3 (less than 4inches)
  ISS
    Not just for ham radio
    Multiple Modes of operation
    Sometimes Astronauts will hop on the radio
  AO-7
    Launched in 1974
    Failed in 1981, came back to life in 2002
    Oldest operational communications satellite
    Used by the anticommunist opposition Fighting Solidarity during martial law in Poland.
Several Operational modes
Telemetry only - Only transmits satellite stats
FM Repeater - works like terrestrial repeater.
  One FM communication channel.
  Easiest to use and most crowded/busy
Linear Transponder
  Translates anything within one frequency range to another frequency range
  Ron Burgundy of space
Digital Repeater
  Decodes and repeats digital communications

## Slide 16: Ham Radio Satellites
FM Repeater Satellite Operation
Technically Easy / Operationally Hard
Has its own language
LEO footprint
Notes: FM repeaters are the easiest
  Single FM signal on uplink frequency
  Satellite retransmits single FM signal on downlink frequency
  Ham satellites use 145MHz up and 430 MHz down, or opposite
Technically Easy
  Requires a hand held radio and antenna with moderate gain
Operationally Hard
  Easy access means lots of people trying
Short contacts in a predetermined format

## Slide 17: Ham Radio Satellites
https://www.amsat.org/status/
Search for frequency information
Check for upcoming passes
Notes: Preparation for using satellites

## Slide 18: Ham Radio Satellites
FM Repeater Satellite Operation
ISS REPEATER |  |  | 
Memory CH | TX Freq | TX CTCSS | RX Freq
n | 145.990 MHz | 67.0 Hz | 437.810 MHz
n+1 | 145.990 MHz | 67.0 Hz | 437.805 MHz
n+2 | 145.990 MHz | 67.0 Hz | 437.800 MHz
n+3 | 145.990 MHz | 67.0 Hz | 437.895 MHz
n+4 | 145.990 MHz | 67.0 Hz | 437.890 MHz
Notes: Configure memory channels for each FM satellite you want to operate
Some will have turn on tones
  you’ll probably never need this

## Slide 19: Ham Radio Satellites
FM Repeater Satellite Operation
ISS REPEATER |  |  | 
Memory CH | TX Freq | TX CTCSS | RX Freq
n | 145.990 MHz | 67.0 Hz | 437.790 MHz
n+1 | 145.990 MHz | 67.0 Hz | 437.795 MHz
n+2 | 145.990 MHz | 67.0 Hz | 437.800 MHz
n+3 | 145.990 MHz | 67.0 Hz | 437.805 MHz
n+4 | 145.990 MHz | 67.0 Hz | 437.810 MHz
Notes: VHF has less shift than UHF

## Slide 20: Ham Radio Satellites
FM Repeater Satellite Operation
Notes: TODO: ADD CONTACT AUDIO

## Slide 21
Notes: TODO: ADD CONTACT AUDIO

## Slide 22: Ham Radio Satellites
QO-100
Online Receiver: https://eshail.batc.org.uk/nb/
Notes: Qatat-OSCAR 100
Geostationary
Narrowband and wideband transponder 2.4GHz up and 10 GHz down
Can send voice and video signals
https://eshail.batc.org.uk/nb/

## Slide 23: Receive Only
SatNOGS
Notes: SatNOGS network of satellite ground stations
Others can use you station for observation when you’re not using it
Requirements: Rpi and RTLSDR

## Slide 24: Receive Only
TinyGS
Notes: Network of receivers like SatNOGS
For LoRa satellites

## Slide 25: GSaaS
AWS and Azure
Notes: Ground Station As A Service from Microsoft and Amazon
Other providers
  Leaf space
  KSAT

## Slide 26: GSaaS
S-Band
X-Band

## Slide 27: GNU Radio projects
gr-iridium
gr-satellites
Notes: gr-iridum: iridium burst detector and demodulator
  ACARS messages
gr-satellites: collection of telemetry decoders that supports many different amateur sats
  Used for building blocks to implement other satellite decoders

## Slide 28: Military Satellites
UHF 240-270 MHz
https://www.wired.com/2009/04/fleetcom/
Notes: UHF milsats
Can be heard with scanner
Fleetsat 8 Navy Sat
Brazil pirates
Sometimes legitimate operators in the clear: Operation Deepfreeze calling back to McCord

## Slide 29: SpaceX Telemetry
r00t (@r2x0t)
Notes: April 2021
R00t was able get spacex telemetry
Spacex and DOD wasn’t happy, encrypted

## Slide 30: HAKUTO-R
Notes: Hah-ku-toe
HAKUTO-R private moonlander
April 25 2023

## Slide 31: Russian Military Satellites
MERIDIAN
Linear Transponders

## Slide 32: Russian Military Satellites
Remember kids, intentional interference is illegal!

## Slide 33: Russian Military Satellites
Remember kids, intentional interference is illegal!
MERIDIAN 7 [40296, 2014-069A] MERIDIAN 8 [44453, 2019-046A] MERIDIAN 9 [45254, 2020-015A]

## Slide 34: Russian Military Satellites
MERIDIAN 7 [40296, 2014-069A] MERIDIAN 8 [44453, 2019-046A] MERIDIAN 9 [45254, 2020-015A]

## Slide 35: Get started
Start with RX
Learn with ham radio satellites